Gents,

To start the camera and operate it at max frame rate, do the following.

First, set the wired IP address to whatever subnet you're running on. You can connect the wifi NIC to the open internet or another wireless network for other connections the internet.

On power up, run these scripts once. After all scripts are run, you can just jump to launching /repos/VimbaX_2023-1/bin/VimbaXViewer

#the sudo password is `aar` (no ticks, just lower case AAR)

#First source an export script for env variables
#Must have the ‘.’ – we are sourcing this .sh script (run it twice!!). The expected output is:
#The second output is what we want!
. /repos/VimbaX_2023-1/cti/SetGenTLPath.sh
. /repos/VimbaX_2023-1/cti/SetGenTLPath.sh
#Then set the MTU to 9000 for “jumbo frames”
sudo ifconfig eth0 down
sudo ifconfig eth0 mtu 9000
sudo ifconfig eth0 up

#DEV_000A4708FDDF is the MAC of the Camera I sent you!
#Set the IP Address of the camera to whatever you’d like
#Must set IP each Power cycle of camera
#Assuming camera is on same LAN, just type:
/repos/VimbaX_2023-1/bin/ConfigIp_VmbC DEV_000A4708FDDF 192.168.1.25 255.255.0.0

#Now launch the viewer. Click on the camera and then click the Play button in the new window that appears.
/repos/VimbaX_2023-1/bin/VimbaXViewer

This should use about 500MB/sec or ~2.5-3 Gbit/sec, which is expected, you can use bmon in another terminal to monitor the network bandwidth usage.

This viewer has a slight latency, our final software will not have this, but we are working w/ the camera vendor to fix a pending bug.